## Slide 1: Unit 1.1 Systems Architecture Lesson 1

## Slide 2: Big Picture
1969 was a famous year for what…..?

## Slide 3: Big Picture
1969 was a famous year for what…..?
https://www.youtube.com/watch?v=PrSD8tpoSz0

## Slide 4: Big Picture
1969 was a famous year for what?
- Man on the Moon
What typical Computing Hardware may be inside the Apollo Guidance Computer?
What would be the brains of the Computer?

## Slide 5: Learning Objectives
To be able to describe the purpose of the CPU
To be able to state the function of the CPU (fetch and execute instructions stored in memory)
To be able to describe how common characteristics of CPUs affect their performance:
  Clock Speed
  Cache Size
  Number of Cores
To understand ‘embedded systems’ regarding:
  Their Purpose
  Be able to give examples

## Slide 6: Engagement Activity
What processing power does your computer at home have? Typically?
Are you aware of the processing power of your mobile phone? Tablet?
How is processing power measured?
Guess at Processing Power of the Apollo Guidance Computer (AGC)
  Compare to iPhone 6

## Slide 7: Key Words
Execute
Embedded System
Clock Speed
Cache
Core
Processor
MHz
GHz
Hertz
Instruction

## Slide 8: What is the Purpose of the Processor?
The processor is “the brains of a Computer System”
It Processes Data
Carries out instructions (Executes Them)
Processors have a Clock speed measured in Hertz
  Number of Cycles Per Second

## Slide 9: Processor Speed
Measured in Hertz (Hz)
Typical Speeds have spanned across MHz and GHz
1GHz Processor executes 1 Billion Instructions per second
2GHz Processor executes 2 Billion Instructions Per Second

## Slide 10: Processor - Cores
Each processor has a “core” in which instructions are executed.
Processors can be multi-core
  Dual Core
  Quad Core
  8 Core
Each core executes instructions independently
Dual Core may execute up to twice as many instructions per second

## Slide 11: Processors – Cache Size
Processors have “Cache” – This is very fast, and usually a very small amount of memory on the processor chip
The Cache acts as an intermediary between the processor and the Main Memory
As programs are executing – the Cache holds commonly used instructions

## Slide 12: Activity 1
Produce a guide explaining the development of the CPU over the last 20 years. Include descriptions of:
  Processor Speed
  Processor Number of Cores
  Processor Cache Size
Within the guide explain the concept of Moore’s Law
Find diagrams of different CPUs – label these

## Slide 13: What affects Performance?
Clock Speed
  Doubling the clock speed will double the number of instructions executed per second
Cores
  Quadrupling the number of cores may quadruple the number of instructions executed per second
Cache Size
  Increasing the cache size will reduce the number of memory to disk transfers and thus may speed up processing of these instructions

## Slide 14: Activity 2
Complete Worksheet on Performance of CPU’s

## Slide 15: Embedded Systems
A computer System that is made up of both Hardware and Software
  Often known as Firmware
Usually for very specialised tasks
Doesn’t usually contain an Operating System
An example: Dishwasher

## Slide 16: Activity 3
Produce a list of embedded systems found around the home
Discuss the purpose of these with your partner
  Would you ever need to write a proper program for these?
  Why do you think that we have embedded systems?
  What are the benefits and drawbacks of embedded systems? Make a list of these for revision.

## Slide 17: Plenary
Questioning
Produce One Question + Mark Scheme
Exit Pass – Describe the purpose of a CPU
Exit Pass – Describe the effect of Number of Cores / Cache Size / Processor Speed on Performance
Homework: Use Resource 1 to study the Apollo 11 Hardware and write a report discussing how the technology has changed over the last 40-50 years.

## Slide 18
OCR Resources: the small print OCR’s resources are provided to support the teaching of OCR specifications, but in no way constitute an endorsed teaching method that is required by the Board, and the decision to use them lies with the individual teacher. Whilst every effort is made to ensure the accuracy of the content, OCR cannot be held responsible for any errors or omissions within these resources. © OCR 2016 - This resource may be freely copied and distributed, as long as the OCR logo and this message remain intact and OCR is acknowledged as the originator of this work.
OCR acknowledges the use of the following content: n/a
Please get in touch if you want to discuss the accessibility of resources we offer to support delivery of our qualifications: resources.feedback@ocr.org.uk